# APPENDIX

MARINE (SCOTLAND) ACT 2010

BEST PRACTICABLE ENVIRONMENTAL OPTION (BPEO) ASSESSMENT: DISCHARGE OF FISH FARM CHEMICAL TREATMENT AGENTS – MANAGEMENT AREA 8c

1.	Introduction

This section should include the following:

  - Background to application

This Best Practicable Environmental Option (BPEO) assessment supports an application for sea disposal licences under the Marine (Scotland) Act 2010.

The aim is to obtain permission to discharge sea lice treatments from wellboats in Scottish Coastal waters, adjacent to cage farm sites operating under CAR Licences issued by SEPA.

In-feed medications, such as Slice, are generally effective and relatively easy to administer.  However, if they are used exclusively there is a risk of reduction in efficacy due to the build up of resistance.  Best practice requires that chemical treatments, including bath treatments, are alternated in order to retain efficacy.

Bath treatments can be logistically challenging, labour intensive and, depending upon the numbers of cage units involved, can take some time to complete a round of treatments. Use of tarpaulins can also be limited to neap tides at more exposed sites. Bath treatments can also pose higher risks to fish welfare when treating at weights approaching harvest size as oxygen levels may become critical (especially so in the summer months, when water temperatures are at their maximum).

The use of wellboat based bath treatments has a number of advantages over the use of tarpaulins.  For example, by using wellboats the risk to fish welfare can be reduced as factors such as oxygen levels and temperature can be monitored and controlled.

In addition, the inclusion of wellboat treatments allows a more comprehensive use of the available bath treatment chemicals.  The use of some bath treatment chemicals, particularly Salmosan, may be limited by discharge consents which are too small to treat the site efficiently using cage enclosure.  This restricts the implementation of a rotational treatment strategy as outlined in the SSPO Code of Good Practice.  Rotation is designed to reduce the risk of resistance developing within the limited medicine choices available.  Wellboats also allow use of hydrogen peroxide which is otherwise very difficult logistically and very dangerous if attempted in full tarps.

Using wellboat treatments appears to be the best possible alternative, where it is practicable and cost effective, to optimise our control of sea lice and maintain high levels of fish welfare.

The use of wellboats to carry out treatments meets objective one of Scotland’s National Marine Plan and reflects the principles of ‘. . . minimizing and mitigating environmental impacts . . .’ (http://www.gov.scot/Resource/0047/00475466.pdf) as outlined in section 7.16 of the Plan. Wellboats allow the effective treatment of sites using lower chemical doses, therefore limiting the amount of chemical discharge to the environment and allowing sustainable use of lice treatments through the rotation of the treatments available.

  - Source of materials

EXCIS

Materials are supplied by: 		Materials are manufactured by:

Novartis Animal Health UK Ltd 		Vericore Ltd

New Cambridge House 			Kinnoull Road

Litlington 					Kingsway West

Nr Royston Dundee 				DD2 3XR

Herts

SG8 0SS

SALMOSAN/SALMOSAN VET

Fish Vet Group

22 Carsegate Rd

Inverness

IV3 8EX

ALPHAMAX

PHARMAQ Ltd                                             PHARMAQ AS

Unit 15                                                          Skogmo Industriomrade

Sandleheath Industrial Estate                      N-7863 OVERHALLA

Fordingbridge                                               Norway

Hampshire

SP6 1PA

PARAMOVE

BRENNTAG (UK) LIMITED

Bilton Way Industrial Est.

Lutterworth

Leicestershire

LE17 4HH

AZASURE

Neptune Pharma Ltd.

Regus House

Victory Way

Admirals Park

Crossways

Dartford

DA2 6QD

England

Chemotherapeutants for the control of sea lice are Prescription Only Medicines (POMs). Only a veterinarian can prescribe the treatment for animals under his/her care.

All therapeutants are licensed in the UK and have full marketing authorisation.

  - Description (nature and volume) of materials

Please refer to the Product Data Sheets/Material Safety Data Sheets below.

EXCIS

ExcisTM is a clear, yellow tinted, cutaneous solution for water borne use, with an alcoholic odour containing 1% w/v Cypermethrin (cis40:trans60).

It is to be administered by addition to seawater.

Treatment dose: 0.5mL/m3 sea water. This is equivalent to 5ug cypermethrin/Litre sea water.

SALMOSAN

Salmosan® is a wettable powder containing 50% w/w azamethiphos which is diluted in water and is administered by addition to seawater.

Treatment dose: 0.2g/m³. This is the equivalent to 100mg/Litre seawater.

Alphamax/AMX

AlphaMax® is a bath concentrate, containing the synthetic pyrethroid deltamethrin which is

capable of blocking impulses in the nervous system of the sea lice resulting in mortality. Contains 1% w/v Deltamethrin.

Treatment dose: 0.2ml/m³ seawater.  This is equivalent to 2ug Deltamethrin/Litre seawater.

SALARTECT

Aqueous solution of Hydrogen Peroxide which is available in 2 strengths, either 35% or 50% hydrogen peroxide. Treatment dose 4.28 or 3.00kg/m³ respectively.

  - Details of previous, related operations including current practice

Please refer to the company Standard Operating Procedures for bath treatment in tarpaulins and wellboats.

All the company’s sites hold appropriate SEPA CAR Licences to discharge these products. Treatments would only be administered within the limits as set out in these Licences (or at another level as determined by Marine Science Scotland).

2.	Discussion of Available Disposal Options

Consideration should be given to the following:

  - Land discharge via an outfall

The volumes of water involved make land discharge practically and technically unfeasible. Availability and proximity of suitable outfalls in operational areas are extremely limiting, and transfer of such water for subsequent release may have disease implications.

2.2	Sea disposal

    - Fish farm cages via CAR consent

CAR consent only allows a limited number of cages to be treated per day.

It requires full enclosure tarpaulins that can be extremely difficult to manage, particularly at 	more exposed/tidal locations.

- Use of tarpaulins can often be limited to a narrow “window” of opportunity, such as slack water and favourable weather conditions.

- Variable volumes may be enclosed by the tarpaulin, which makes dose rates difficult to determine

    - Fish farm cages via Marine Licence

Wellboats allow the farmer to treat fish in a controlled environment. Treatment volumes are well defined and therefore dose rates and efficacy of treatments are more predictable and more consistent. On-board oxygenation systems allow better control of oxygen levels in the treatment water and are therefore beneficial to fish welfare.

    - Location other than at fish farm cages

N/A at present

    - Pre-treatment options prior to discharge at sea

There are no known pre-treatment options prior to discharge at sea. The discontinuous discharge may allow discharges at specific points in the tidal cycle if required. Cypermethrin has low water solubility and degrades rapidly. It binds strongly to organic particles and other solids, and it is rapidly adsorbed by sediments, reducing its biological availability and hence its toxicity to benthic organisms. Cypermethrin released following a bath treatment will be rapidly diluted in the receiving environment and the majority will be adsorbed onto particulate material, which will settle to the seabed.

As with Cypermethrin, Deltamethrin is also highly insoluble in water and is adsorbed by sediments giving it a half-life of 2-4 hours within the water column.

Azamethiphos is an organophosphate which is moderately water soluble with no bioaccumulation or biomagnifications. When released into the environment following a bath treatment it remains in the aqueous phase until it is broken down into non-toxic derivatives (SEPA Annex G).  Azamethiphos has a half-life of 10.8 days at 20°C in water.

Hydrogen Peroxide degrades rapidly breaking down to water and oxygen and presents no long-term hazards to marine life.

CAR Licences currently specify the limits of each chemical which may be released untreated into the wider environment, taking into account initial dilution effects and the hydrographic conditions at each site. We are not proposing to exceed these limits in any way.

3.	Aspects to be taken into Consideration

For each option identified, the assessment should include reference to the following:

3.1	Strategic considerations

    - Operational aspects, including handling, transport etc

All treatments are under veterinary supervision and/or instruction.

All operations are carried out following written Standard Operating Procedures (please refer to attached documentation).

    - Availability of suitable sites/facilities

Responsibility of the Regional Production Manager to hire a suitable wellboat under contract to SSF. Where possible, treatments would be combined with other fish handling activities to minimise stress to the stock.

    - Legislative implications, both national and international

Marine Licence, discharges within specified limits. All sites currently hold CAR Licences which permit discharge of the chemicals applied for here.

3.1.4	Summary of the outcome of discussions with third parties (If possible, copies 		of consultees replies should be appended to the assessment)

There have been no formal discussions with third parties. However, all sites are part of, or working towards an Area Management Agreement. All stakeholders (including wild fisheries) strive to achieve optimal control over sea lice infestations.

3.2	Environmental considerations

    - Safety implications

Please refer to the Material Safety Data Sheets and Standard Operating Procedures.

    - Public health implications

The only Public Health implication identified relates to Food Safety, with consumption of medicated fish. With Prescription Only Medicines, all treated fish undergo a withdrawal period (as per manufacturer’s instructions) prior to slaughter. Farming traceability system ensures this period is adhered to prior to harvesting.

    - Pollution/contamination implications, including discussion on: accumulation, toxicity, hazards, persistence, short and long-term impacts, dilution and dispersion, etc

The Scottish Environment Protection Agency (SEPA) has introduced new thresholds for medicines used to treat sea lice infestations in marine fish farms.

It follows the publication in 2005 of a five-year study monitoring and measuring the potential environmental impacts of using sea lice medicines. The independent PAMP* report confirmed there was no evidence of any impact from these substances on the environment which could be separated from the natural variation found in marine ecosystems.

The use of the revised modeling approach removes some of the precaution in the way that the sea lice treatment Excis is licensed, allowing fish farmers to more effectively treat sea lice infestations at marine cage fish farms. More effective treatment of such infestations may lead to benefits for wild salmon populations, as there are anecdotal links between declines in salmon populations and the occurrence of sea lice on wild salmon.

Full details of the PAMP report are available at:

http://www.sams.ac.uk/research/coastal%20imapcts/ecol.htm

And the revised modeling documentation can be found at:

http://www.sepa.org.uk/pdf/guidance/fish_farm_manual/annex/G.pdf

Copies of the CAR Licences for each site are appended to each application.

    - Interference with other legitimate activities, e.g. fishing operations, other aquaculture interests

Treatments are carried out in accordance with SSPO CoGP recommendations  and co-ordinated with other sites within this disease management area

Licencing of wellboat treatments on-site is not expected to have any significant effects upon any third party. There may be an element of slightly increased traffic and increased presence of the wellboat(s) on-site, but this should not adversely affect other users. No increased use, or discharge of chemicals is proposed.

    - Amenity/aesthetic implications

None, with the exception of the physical presence of the well-boat on-site.

    - Best practice guidance and mitigation measures

Wellboats allow for absolute control of treatment volume and dose rates, facilitating much more efficient and consistent treatments.

Wellboat treatments also allow much better control of oxygen levels and are therefore of benefit to fish welfare.

By using the wellboats for bath treatments the amount of chemical used is greatly reduced due to the lesser volume of the wellboat tanks compared to that of the raised cages (i.e for 1 80m circ cage raised to a depth of 4m has a volume of 2370m³ which would require 1.185l of Excis compared to using two tanks on a wellboat with a total volume of 625m³ (Ronja Skye) which would only require 0.3125l of Excis.

3.3	Cost considerations

    - Capital costs, e.g. site costs, transport hire/purchase costs, equipment hire/purchase costs etc.

- Capital cost: None

- Hire cost:

Hiring a large vessel comes at a cost of £7000-9000/24 hours depending on size of boat.

Tarpaulins require buying oxygen and renting diffusion systems (approx. £2,000).

- Purchase:

Chemical cost is up to £3,000 per site if using a boat

Chemical cost is up to £12,000 per site when using tarpaulins.

3.3.2  Operating costs, e.g. labour costs, site operation costs, transport costs,   equipment costs, environmental monitoring costs etc.

- Operating costs are unchanged

- Labour cost remains unchanged if not lower since less handling is required.

- Starvation period must be increased from 1 day when using a tarpaulin to 2-3 days when using a boat. This means a loss of growth for 1-2 days or a loss of growth of up to 15g per day per fish] (ca. £1125 per cage per day).

- There are no environmental monitoring costs incurred although it is possible some           treatments will be monitored with dosage of Cypermethrin in the water.

4.	Conclusions

  - Summary of available options

The only two options to discharge are either under SEPA/CAR licence or under the appropriate Marine licence.

  - Summary of pros and cons of each option

The following table summarise aspects of each scenario:

| Options | Cost | Chemical usage | Technical difficulty | Logistics | Environmental impact | Treatment efficacy | Risk to livestock | Strategic acceptability |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Tarpaulins – CAR consent | High | High | Very labour intensive. | Weather and tidal restrictions apply | Moderate | Good | High | Moderate |
| Wellboat – Marine Licence | High | Moderate | Less labour intensive and more efficient | Boat availability and size, adverse weather conditions | Low | Good | Moderate to High | High |

  - Identification of BPEO

There are a number of advantages of being able to carry out treatments with a wellboat over a treatment using tarps.  Due to the smaller volume of the tanks much smaller quantities of chemical are required resulting in less chemical being discharged to the environment and lower chemical costs.  Wellboats also allow treatment to be carried out in a controlled and monitored environment which reduces the stress on the fish.  This has to be set against limited wellboat availability and very high financial cost of using wellboats.

We trust this will be considered an acceptable option under the terms of the Marine (Scotland) Act 2010.